## Slide 1
21.04.2020
APPLICATIONS OF COMPLEX NUMBERS, INVERSE TRIGONOMETRICAL FUNCTIONS AND SECOND-ORDER CURVES
Viktor Bolgov, D.Sc., Phone: +372 53887671, e-mail: victor_bolgov@yahoo.com
Estonian Maritime Academy / Centre for General and Basic Studies
Tallinn University of Technology

## Slide 2
There are two types of electrical power supplies used both on board of ships and on the mainland: direct current (DC) and alternating current (AC). Let us assume that we apply either DC or AC voltage to a resistor R. Resistive element R models transformation of electrical energy into any other form of energy: mechanical, thermal, lighting, chemical, etc.
DC is used in electronics, electrical vehicles, local networks with renewable energy sources, submarine cables etc.
AC is used in the vast majority of power transmissions and distribution networks, electrical machines and electrotechnological installations.
DC current and voltage are unipolar. AC current and voltage varies in the value and polarity over the time.
If a direct voltage U is applied to a resistor with resistance R it will cause a direct current I flowing in the circuit. Both voltage and current are unipolar and related to each other by means of Ohm’s law
Complex numbers in electrical circuits
Introduction into DC and DC
The power dissipating in the resistor R can be found by using Joule-Lenz law

## Slide 3
Complex numbers in electrical circuits
Generation of sinusoidal EMF
Electric generators induce an electromotive force (EMF) by rotating a loop in a magnetic field. When this generator loop is rotated from the Postion 1 to the Postiton 3 around the axis OO’, the magnetic flux Φ passing the loop internal ares changes from its maximum value to zero, inducing an EMF.
When the coil side conductors 12 and 34 cut magnet flux lines, EMFs e1 and e2 are generated producing resultant EMF e = e1 + e2 at the coil terminals A and B.
Faraday’s law of induction is used to find the emf induced:
where dΦ is change of magnetic flux through the coil 1234 over the time dt.
Int he Position1 the magnetix fux is of maximum value
Φm=2rlB,
where r is the radius of the coil (m), l – the active coil lengths 12 and 34 pikkus (m), B – magnetix flux density (T).
To find the time dependence of EMF, we assume the loop rotates at a constant angular velocity ω. The angle α is related to angular velocity by α = ωt.
The magnetic flux at any position can be found as
The total EMF around the loop is then

## Slide 4
Complex numbers in electrical circuits
Generation of sinusoidal EMF

## Slide 5
Complex numbers in electrical circuits
Introduction into aC
The alternating voltage is usually a sine wave with the maximum value or amplitude Um that can mathematically be described as follows
u = Um sin ωt = Um sin 2πft
where u is the instantaneous value of the voltage (V) at the time instant t (s), f is the frequency of sine wave (Hz), ω = 2πf is the angular frequency (rad/s). The frequency f can be found via the period T (s) of the sine wave in the next way
That means Such a sine voltage being applied to a resistor R causes an alternating current i
i = Im sin ωt = Im sin 2πft
where i is the instantaneous current value (A) at the time instant t (s), Im is the amplitude of the current.
At each instant of time, there is relationship between instantaneous values of the voltage and current according to Ohm’s law
Since maximum values are also instant ones, there is valid
Let us find the amplitudes of the alternating current and voltage that produce the same power P dissipation as happens in the resistance R under the direct voltage U and current I. In electrical engineering theory, it is found that the sinusoidal voltage u and current i with amplitudes
and
produce the power P in the AC circuit equal to the DC power caused by U and I in the DC circuit
The values of alternating voltage and current that are equivalents to DC values and found as follows
and
and they are named rms or effective values.

## Slide 6
Complex numbers in electrical circuits
Phasor of sine wave
There is a set of mathematical tools developed for DC circuits that could be applied to AC cses. The application of Ohm’s and Kirchhoff’s laws to each instant of an alternating sine wave is a vast and complicated task. One way to facilitate the use of DC circuit laws in AC circuits is the application of effective values instead of amplitudes. However, it is not enough. The alternating nature of sine waves creates complex electromagnetic field around AC circuits that creates time (angle) shifts between voltages and currents. To represent and calculate those shifts, there was proposed the substitution of sine values with their rotating vectors also known as phasors. Let us consider how to substitute a sinusoidal current i = Im sinωt with its phasor.
If a vector with the magnitude Im is placed on a Cartesian plane and rotates counter clockwise around the point O with the angular velocity ω then it can be described in polar and trigonometrical form as
Im = Im ejωt = Im cosωt + jIm sinωt,
where Im is the complex amplitude, j is the electrical notation for the imaginary quantity denoted in mathematics as i, ω is the angular velocity that is equal to the angular frequency of the alternating current.
Thus, a complex number Im is obtained. Using the complex plane, we can envision the behaviour of this complex parameter. The magnitude of the complex amplitude is OA, and the initial angle is equal to zero at t = 0 s. As time increases, the locus of points traced by the complex amplitude creates a circle with the constant magnitude of OA. The number of times per second Im goes around the circle equals to the frequency f. The time taken to go around the circle once is period T.
The projections of Im onto the real x and imaginary y-axes give us the real and imaginary parts of the complex amplitude. There is an interest towards the imaginary part of the complex amplitude in electrical engineering.
Im[Im ejωt] = Im[Im cosωt + jIm sinωt] = Im sinωt = i.

## Slide 7
If the vector OA is under the angle Ψ at the time instant t0 = 0 s then its initial value is not equal to zero i0 = Im sin(ωt0 + Ψ) = Im sinΨ (since ωt0 = 0°).
The common expression for the sine waveform is as follows
i = Im sin(ωt + Ψ),
where Ψ is the initial phase.
The corresponding phasor in a complex form in this case looks like
Im = Im ej(ωt + Ψ)= Im cos(ωt + Ψ) + jIm sin(ωt + Ψ).
Complex numbers in electrical circuits
Phasor of sine wave
Therefore, any alternating current of a sinusoidal waveform may be described with a phasor rotating with the angular speed that equals to the angular frequency of the sine wave. Those phasor notations differ in different textbooks and could be, for example
.
In electrical engineering, there is a traditional way to present a complex vector with its amplitude and initial phase keeping in mind that it rotates with the angular frequency ω
For example the notation
A means the current with the amplitude of 5 A is shifted by the 30° in relation to the y-axis.

## Slide 8
Phasors on a complex plane are called vector or phasor diagram. There are two sinusoidal currents i1 and i2 on the right side in Figure. Their phasors are presented on the left side. The y-axis of a complex plane is called imaginary axis and has notation “+j” while x-axis is called real one and denoted as “+1”.
Let us explore how one can use phasors in electrical calculations. There is a node between three branches with currents i1, i2 and i3 (Fig. 1.7, a). For example, the currents i1 and i2 flow through two separate cables to some loads and i1 is the current of a ship’s main busbar. The currents i1 and i2 are known and the current i3 is unknown. According to Kirchhoff’s, law those node currents are interrelated at any time instant
Complex numbers in electrical circuits
Addition of phasors
The sine waves i1 and i2 has different initial angles, i.e. their complex amplitudes may be expressed as
Im1 = Im1∠Ψ1 and Im2 = Im2∠Ψ2.
The current i1 leads the current i2 and there is a phase shift between them φ = Ψ1 – Ψ2. This phase shift is also seen from their vector diagram, i.e. it is the angle between phasors Im1 and Im2.
Instead of calculating the sum i1+i2 at each time instant the phasors Im1 and Im2 can be added to each other to get the resultant phasor Im3
Im3 = Im1 + Im2.
The projections of the complex amplitude Im3 onto axes x (real axis +1) and y (imaginary axis +j) can be found by using trigonometrical functions
Im3 = Im1 + Im2 = Im1 cos(ωt + Ψ1) + Im2 cos(ωt + Ψ2) + j{cos(ωt + Ψ1) + Im2 cos(ωt + Ψ2)} = Im3 ∠Ψ3,
where the amplitude of the current i3 is found by means of Pythagoras theorem
and the phase angle – by means of some inverse trigonometrical function, e.g.

## Slide 9
It must be noted, that in practical electrical calculations phasors are usually mot expressed by using amplitudes of electrical state parameters, but with their effective (rms) values.
If to apply a sinusoidal voltage u to a resistance R then a sine wave of a current i immediately appears without any time delay, which value may be found by means of Ohm’i law
Therefore, there is no phase shift between their vectors and Ohm’s law can be rewritten either via amplitudes
or, being divided by , via effective values like in DC circuits
The ability of an AC current to store magnetic field energy around a conductor is characterised by its inductance L and inductive reactance XL = ωL = 2πfL. As a result, the current lags voltage by angle π/2 or 90°. This lag can be briefly and clearly presented by means of complex values. If a voltage u is supposed to be with a phase of 0° then Ohm’s law for effective complex values can be written like this
where –j = e-j90° is the operator shifting the complex current I back in relation to U by 90° or π/2 .
Complex numbers in electrical circuits
Resistance and Inductive reactance

## Slide 10
The ability of an AC current to store electric field energy around a conductor is characterised by its capacitance C and capacitive reactance
As a result, the current i leads the voltage u by angle π/2 or 90°. This phase shift can be clearly presented by means of complex values. If voltage u is supposed to be with a phase of 0° then Ohm’s law for effective complex values can be written in the next way
where j = ej90° is the operator shifting complex current I in relation to U ahead by 90° or π/2 .
Practical loads on board of ships and in ports (electrical motors, lighting installations, etc.) may usually be modelled by a series combination of resistance R and inductive reactance XL.
Complex numbers in electrical circuits
Capacitive reactance amd impedance
There is no phase shift between the current and the voltage drop across the resistance R. Thus, the voltage drop Ua is in phase with the current I. The voltage drop over the inductive reactance UL leads the current I.
According to Kirchhoff’s second law, the input voltage U may be found as
U = Ua+UL.

## Slide 11
Complex numbers in electrical circuits
impedance AND
If the phase of the current phasor I is equal to 0° then the voltages can be presented as follows:
a) Resistive voltage drop Ua = I·R = I R ej0° = Uaej0°,
b) Inductive voltage drop UL = I·jXL = I XLej90° = ULej90°,
c) Input voltage U = I(R+jXL) = I·R + I·jXL= Uaej0°+ULej90° = Uejφ.
Let us have a closer look at the last expression. The sum R + jXL is named impedance Z = Z ejφ, which is a complex number with the magnitude
and the argument or phase
It is better seen from so-called impedance triangle constituted by resistance, reactance and impedance
Therefore, Ohm’s law in the most common form is as follows
U = I·Z = IZejφ = Uejφ.
That means it is the impedance phase φ defines phase shift between the terminal voltage u and the current i.
Example
As shown in Fig. 1.11, a, there are a resistor with resistance R = 4 Ω, an inductor with inductive reactance XL = 3 Ω and the current I = 1 A.
Find impedance Z, voltages across resistance Ua, reactance UL, and a terminal voltage U.
Solution:
Impedance may be found as follows Z = R + jXL = 4 + j3 Ω.
According to the Pythagorean Theorem impedance magnitude
Its argument
Hence, the complex value of impedance Z = Z ejφ= 5 ej36.9° Ω.
Voltages may be found by means of Ohm’s law in a complex form.
The voltage across the resistor Ua = I·R = IR ej0° = 1·4 ej0°= 4ej0° = 4 V.
The voltage across the reactance UL = I·jXL = IXL ej90° = 1·3ej90°= 3ej90° V.
The terminal or input voltage UL = I·Z = IZejφ = 1·5ej36.9°= 5ej36.9° V.

## Slide 12
Inverse trigonometrical functions are a vital part of electrical engineering and any other science using complex numbers. For example in the RL circuit, there is phase shift φ = ΨU – ΨI between an input voltage U and a current I as well as in the impedance triangle between resistance R and impedance Z. It means one needs to calculate the angle φ in order to present terminal voltage or impedance in a complex form, i.e. correspondingly U = U ejφ and Z = Z ejφ.
Inverse trigonometrical functions in electrical circuits
As a result, there are several opportunities to find the phase shift angle φ:

## Slide 13
There is always concern about decreasing active power losses in electrical networks. It reduces bills for electricity for mainland customers and the consumption of the fuel on board of ships. One of tasks related to active power saving is the choosing of the proper configuration of the electrical substation.
A distributing substation usually contains two transformers that steps down middle voltage U1 of 6…35 kV to low voltage U2 = 0.4 kV. That is the case for port network and for many ships with the on-board gird containing a high-voltage part.
Second order curves and optimal operation of electrical substation
Each transformer has at least two windings: middle voltage (ML) and low voltage (LV) ones. Those are wound around a magnetic core that facilitates energy transfer from MV side to LV side. The active power losses have place in each of the transformer component.
The active power loss in magnetic core ∆P0 is called core loss or no-load loss and it is supposed to be almost constant. It is because this loss depends on voltage U1 that is kept as stiff as possible. That is why the iron loss is often modelled as a constant power load.
The active power losses in MV and LV windings called copper losses are often considered together and they happens in aggregated resistance R of both the windings called short-circuit resistance. This variable loss depends on loading of a transformer, i.e. on the load current I flowing through the windings to consumers. That is why it is also called load loss and may be calculated as follows:
a) Single-phase transformer ∆Pload = I2R;
b) Three-phase transformer ∆Pload = 3I2R.
The total active power loss in transformer can be found in this way:
a) Single-phase case ∆PI = ∆P0 + I2R;
b) Three-phase case ∆PI = ∆P0 + 3I2R.

## Slide 14
It is clear that total active power loss in transformer depends on the squared load current forming a parabolic curve shifted upwards by amount of no-load active loss (curve PI). If two similar transformers operates in parallel then the total loss in substation transformers (curve PI+II) may be calculated in the next way:
Single-phase case
Three-phase case
The optimal choice of the substation configuration, i.e. whether to keep in operation one or two transformers in parallel connection in order to get minimum active power loss, depends on some boundary load current Ilimit. If the load current is less than Ilimit then the operation with a single transformer is preferable. If the load current is greater than Ilimit then the substation configuration with two operating transformers gives less loss of active power.
Second order curves and optimal operation of electrical substation
Example
There are two three-phase transformers at the substation with the following parameters:
Nominal power: 1000 kVA
Nominal voltages: 10.5/0.4 kV
No-load loss: ∆P0 = 1700 W
Short-circuit resistance: R = 2.4 Ω.
Find at which boundary load current Ilimit the substation should be switched from the operation with a single transformer to the operation with two transformers in parallel.
Solution: The active power loss under operation with a single transformer can be expressed as
∆PI = ∆P0 + 3RI2 = 1700 + 7.2I2 (curve PI).
In the case of two transformers in parallel connection, the active power loss depends on current as follows
(curve PI+II)
The intersection point of two parabolas gives us the value of Ilimit. It can be found by equating the expressions for ∆PI and ∆PI+II

## Slide 15
Näide 2. HARGNEV RLC-ahel
Vaatleme kahest rööpaharust koosnevat ahelat, kusjuures kumbki haru omab aktiivtakistust ja reaktiivtakistust (üks on induktiivse ja teine on mahtuvusliku iseloomuga). Tuleb arvutada skeemi talitluse.
Antud: R1 = 60 Ω, R2 = 80 Ω, XL1 = 80 Ω, XC2 = –60 Ω, QC2 = – 60 var.
Leida: Voolud, võimsustegur, nurk φ, võimsused S, P, Q, ahela näivtakistus Z, näivjuhtivus Y.
Lahendused:
Kuna harud 1 ja 2 on ühendatud rööbiti, siis nende peal on sama pinge U. Kui me leiame pinge ühe haru peal, siis on leitud ka pinge teisel harul. Harupinge määramiseks Ohm’i seaduse abil on vaja teada haru takistust ja voolu. On antud mahtuvusvõimsus (miinusmärgiga) teise haru mahtuvelemendis. Seega on võimalik kirjutada
Leiame teise haru näivtakistuse
Siit leiame Ohm’i seaduse alusel U = Z2I2 = 100·1 = 100 V.
Vool esimese harus on samuti leitav Ohm’i seaduse alusel. Selle rakendamiseks on vajalik haru takistus
Siis esimese haru vool
Kuigi voolude I1 ja I2 efektiivväärtused on samasugused, nende nurgad pingega on erinevad
Nagu on näha, erinevalt arkuskoosinusist arkustangens annab nurga märki. Kuna φ1 > 0, siis vool I1 jääb maha pingest U ehk omab aktiivinduktiivset iseloomu. Negatiivne nurk φ2 < 0 näitab, et vool teises harus I2 edestab pinget U, ehk haru omab aktiivmahtuvuslikku iseloomu. Need vektorid on kujutatud joonisel.
Esimese Kirchhoff’i seaduse alusel on sisendvool võrdne haruvoolude geomeetrilise summaga
I = I1 + I2.
Selleks, et leida summaarset ehk sisendvoolu I saab kasutada erinevaid meetodeid. Vaatleme, kuidas saab liita vektoreid nende koordinaatide või projektsioonide abil.
Voolu I1 aktiivkomponent Ia1, mis ühtib pingega U, on leitav järgmiselt
Ia1 = I1 cos φ1 = 1·cos 53,13° = 0,6 A.
Voolu I1 induktiivkomponent Ia1, mis jääb maha pingest U täisnurga võrra, leitakse niimoodi
IL1 = I1 sin φ1 = 1· sin 53,13° = 0,8 A.
Voolu I2 aktiivkomponent Ia2, mis ühtib pingega U, on leitav järgmiselt
Ia2 = I2 cos φ2 = 1· cos (–36,87°) = 0,8 A.
Voolu I2 reaktiivkomponent Ia2, mis edestab pinget U täisnurga võrra, on leitav niiviisi
Ia2 = I2 sin φ2 = 1·sin (–36,87°) = –0,6 A.
Otsitava voolu I aktiivkomponent Ia = Ia1 + Ia2 = 0,6 + 0,8 = 1,4 A.
Otsitava voolu I reaktiivkomponent Ir = IL1 + IC2 = 0,8 – 0,6 = 0,2 A.

## Slide 16
T
thank you for your attention!
Viktor Bolgov, D.Sc., e-mail: victor_bolgov@yahoo.com
Estonian Maritime Academy / Centre for General and Basic Studies
Tallinn University of Technology
o
k